## Slide 1: ARM (and low-power architectures)
CSCI 370 – Computer Architecture
ARM
Advanced RISC Machines

## Slide 2: Main features of the ARM Instruction Set
All instructions are 32 bits long.
Most instructions execute in a single cycle.
Every instruction can be conditionally executed.
A load/store architecture
  Data processing instructions act only on registers
    Three operand format
    Combined ALU and shifter for high speed bit manipulation
  Specific memory access instructions with powerful auto-indexing addressing modes.
    32 bit and 8 bit data types
      and also 16 bit data types on ARM Architecture v4.
    Flexible multiple register load and store instructions
Instruction set extension via coprocessors

## Slide 3: Condition Flags
Logical Instruction Arithmetic Instruction
Flag
Negative No meaning Bit 31 of the result has been set
(N=‘1’) Indicates a negative number in
signed operations
Zero Result is all zeroes Result of operation was zero
(Z=‘1’)
Carry After Shift operation Result was greater than 32 bits
(C=‘1’) ‘1’ was left in carry flag
oVerflow No meaning Result was greater than 31 bits
(V=‘1’) Indicates a possible corruption of
the sign bit in signed numbers
Notes: N flag SUB r0, r1, r2 where r1<r2
Z flag SUB r0, r1, r2 where r1=r2 (also used for results of logical operations)
C flag ADD r0, r1, r2 where r1+r2>0xFFFFFFFF
V flag ADD r0, r1, r2 where r1+r2>0x7FFFFFFF
(if numbers are signed, ALU sign bit will be corrupted)
(0x7FFFFFF+0x00000001=0x80000000)
(answer okay for unsigned but wrong for signed)

## Slide 4: ARM Instruction Set Format
Instruction type
Data processing / PSR Transfer
Multiply
Long Multiply (v3M / v4 only)
Swap
Load/Store Byte/Word
Load/Store Multiple
Halfword transfer : Immediate offset (v4 only)
Halfword transfer: Register offset (v4 only)
Branch
Branch Exchange (v4T only)
Coprocessor data transfer
Coprocessor data operation
Coprocessor register transfer
Software interrupt
Cond 0 0 I Opcode S Rn Rd Operand2
Cond 0 0 0 0 0 0 A S Rd Rn Rs 1 0 0 1 Rm
Cond 0 0 0 1 0 B 0 0 Rn Rd 0 0 0 0 1 0 0 1 Rm
Cond 0 1 I P U B W L Rn Rd Offset
Cond 1 0 0 P U S W L Rn Register List
Cond 0 0 0 0 1 U A S RdHi RdLo Rs 1 0 0 1 Rm
Cond 0 0 0 P U 1 W L Rn Rd Offset1 1 S H 1 Offset2
Cond 1 0 1 L Offset
Cond 1 1 0 P U N W L Rn CRd CPNum Offset
Cond 1 1 1 0 Op1 CRn CRd CPNum Op2 0 CRm
Cond 1 1 1 0 Op1 L CRn Rd CPNum Op2 1 CRm
Cond 1 1 1 1 SWI Number
Cond 0 0 0 1 0 0 1 0 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 1 Rn
Cond 0 0 0 P U 0 W L Rn Rd 0 0 0 0 1 S H 1 Rm
31
28
27
16
15
8
7
0

## Slide 5: Conditional Execution
Most instruction sets only allow branches to be executed conditionally.
However by reusing the condition evaluation hardware, ARM effectively increases number of instructions.
  All instructions contain a condition field which determines whether the CPU will execute them.
  Non-executed instructions soak up 1 cycle.
    Still have to complete cycle so as to allow fetching and decoding of following instructions.
This removes the need for many branches, which stall the pipeline (3 cycles to refill).
  Allows very dense in-line code, without branches.
  The Time penalty of not executing several conditional instructions is frequently less than overhead of the branch or subroutine call that would otherwise be needed.

## Slide 6: The Condition Field
1001 = LS - C clear or Z (set unsigned lower or same)
1010 = GE - N set and V set, or N clear and V clear (>or =)
1011 = LT - N set and V clear, or N clear and V set (>)
1100 = GT - Z clear, and either N set and V set, or N clear and V set (>)
1101 = LE - Z set, or N set and V clear,or N clear and V set (<, or =)
1110 = AL - always
1111 = NV - reserved.
28
31
24
20
16
12
8
4
0
Cond
0000 = EQ - Z set (equal)
0001 = NE - Z clear (not equal)
0010 = HS / CS - C set (unsigned higher or same)
0011 = LO / CC - C clear (unsigned lower)
0100 = MI -N set (negative)
0101 = PL - N clear (positive or zero)
0110 = VS - V set (overflow)
0111 = VC - V clear (no overflow)
1000 = HI - C set and Z clear (unsigned higher)
Notes: 4 bit Condition Field refers to the values of the appropriate bits in the CPSR, as indicated on slide.
Most instructions assembled with default condition code "always" (1110, AL).
  This means the instruction will be executed irrespective of the flags in CPSR.
The "never" code (1111, NV) is reserved.
  This family of conditions will be redefined for future use in other ARM devices.
  Use MOV r0, r0 as NOP operation.
Conditional instructions aids code density
  remove need for many branches (discussed earlier)

## Slide 7: Using and updating the Condition Field
To execute an instruction conditionally, simply postfix it with the appropriate condition:
  For example an add instruction takes the form:
    ADD r0,r1,r2 ; r0 = r1 + r2 (ADDAL)
  To execute this only if the zero flag is set:
    ADDEQ r0,r1,r2 ; If zero flag set then… ; ... r0 = r1 + r2
By default, data processing operations do not affect the condition flags (apart from the comparisons where this is the only effect). To cause the condition flags to be updated, the S bit of the instruction needs to be set by postfixing the instruction (and any condition code) with an “S”.
  For example to add two numbers and set the condition flags:
    ADDS r0,r1,r2 ; r0 = r1 + r2 ; ... and set flags

## Slide 8: Arithmetic Operations
Operations are:
  ADD operand1 + operand2
  ADC operand1 + operand2 + carry
  SUB operand1 - operand2
  SBC operand1 - operand2 + carry -1
  RSB operand2 - operand1
  RSC operand2 - operand1 + carry - 1
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples
  ADD r0, r1, r2
  SUBGT r3, r3, #1
  RSBLES r4, r5, #5

## Slide 9: Comparisons
The only effect of the comparisons is to
  UPDATE THE CONDITION FLAGS. Thus no need to set S bit.
Operations are:
  CMP operand1 - operand2, but result not written
  CMN operand1 + operand2, but result not written
  TST operand1 AND operand2, but result not written
  TEQ operand1 EOR operand2, but result not written
Syntax:
  <Operation>{<cond>} Rn, Operand2
Examples:
  CMP r0, r1
  TSTEQ r2, #5

## Slide 10: Logical Operations
Operations are:
  AND operand1 AND operand2
  EOR operand1 EOR operand2
  ORR operand1 OR operand2
  BIC operand1 AND NOT operand2 [ie bit clear]
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples:
  AND r0, r1, r2
  BICEQ r2, r3, #7
  EORS r1,r3,r0

## Slide 11: Data Movement
Operations are:
  MOV operand2
  MVN NOT operand2
Note that these make no use of operand1.
Syntax:
  <Operation>{<cond>}{S} Rd, Operand2
Examples:
  MOV r0, r1
  MOVS r2, #10
  MVNEQ r1,#0

## Slide 12: The Barrel Shifter
The ARM doesn’t have actual shift instructions.
Instead it has a barrel shifter which provides a mechanism to carry out shifts as part of other instructions.
So what operations does the barrel shifter support?

## Slide 13: Barrel Shifter - Left Shift
Shifts left by the specified amount (multiplies by powers of two) e.g.
  LSL #5 = multiply by 32
Logical Shift Left (LSL)
Destination
CF
0
Notes: Effectively x 2n.
  bits of operand shifted left by specified number of bits.
  Zeros are inserted into the right most end of the word
  last bit removed from the left most end placed in carry flag.
LSL #0 does nothing and is the default shift if none is specified.

## Slide 14: Barrel Shifter - Right Shifts
Logical Shift Right
Shifts right by the specified amount (divides by powers of two) e.g.
LSR #5 = divide by 32
Arithmetic Shift Right
Shifts right (divides by powers of two) and preserves the sign bit, for 2's complement operations. e.g.
ASR #5 = divide by 32
Destination
CF
Destination
CF
Logical Shift Right
Arithmetic Shift Right
...0
Sign bit shifted in
Notes: LSR moves each bit of the register (Rm) to the right by the specified amount.
eg / LSR #5
  all bits are moved 5 places to right (i.e. into less significant positions).
  most significant positions then filled with zeros
  least significant five bits of Rm are removed. The last of these five bits becomes the shifter Carry output, and may set the CPSR's C flag (when the ALU operation is in the logical class).
An LSR 0 is translated into an LSR 32, to put bit 31 of the word into the carry flag.
ASR similar to LSR except that
  high bits are filled with bit 31 of Rm (the sign bit) instead of zeros.
  This preserves the sign in 2's complement notation.
eg/
  Divide a 2's complement number 10000010B (or -126) in Ra by 2.
MOV Ra, Ra, ASR #2
  From Ra=10000010B we get RA=11000001B (or - 63)
An ASR #0 is translated into an ASR #32, to propagate bit 31 of the word into every bit in the word as well as the carry flag.

## Slide 15: Barrel Shifter - Rotations
Rotate Right (ROR)
• Similar to an ASR but the bits wrap around as they leave the LSB and appear as the MSB.
e.g. ROR #5
Note the last bit rotated is also used as the Carry Out.
Rotate Right Extended (RRX)
• This operation uses the CPSR C flag as a 33rd bit.
Rotates right by 1 bit. Encoded as ROR #0.
Destination
CF
Rotate Right
Destination
CF
Rotate Right through Carry
Notes: Rotate Right (ROR), and Rotate Right Extended (RRX) operations
  used to manipulate the bits in a register without destroying those bits.
  move each bit of the register (Rm) by the specified amount.
  eg/ ROR #5
    all bits moved 5 places to the right (i.e. into less significant positions).
  However, rather than being discarded the bits shifted out are then rotated back to other high of the register
    in ROR the bit previously at [0] is rotated to the MSB, [31]
    In RRX - Carry flag included as a 33rd bit in the operation. Bit 0 becomes the Carry out, while the C becomes the MSB
RRX actually encoded as ROR #0
  Example of use: in random number generator given in datasheet
.

## Slide 16: Using the Barrel Shifter: The Second Operand
Register, optionally with shift operation applied.
Shift value can be either be:
  5 bit unsigned integer
  Specified in bottom byte of another register.
Immediate value
  8 bit number
  Can be rotated right through an even number of positions.
  Assembler will calculate rotate for you from constant.
Operand 1
Result
ALU
Barrel Shifter
Operand 2

## Slide 17: Second Operand : Shifted Register
The amount by which the register is to be shifted is contained in either:
  the immediate 5-bit field in the instruction
    NO OVERHEAD
    Shift is done for free - executes in single cycle.
  the bottom byte of a register (not PC)
    Then takes extra cycle to execute
    ARM doesn’t have enough read ports to read 3 registers at once.
    Then same as on other processors where shift is separate instruction.
If no shift is specified then a default shift is applied: LSL #0
  i.e. barrel shifter has no effect on value in register.

## Slide 18: Second Operand : Using a Shifted Register
Using a multiplication instruction to multiply by a constant means first loading the constant into a register and then waiting a number of internal cycles for the instruction to complete.
A more optimum solution can often be found by using some combination of MOVs, ADDs, SUBs and RSBs with shifts.
  Multiplications by a constant equal to a ((power of 2) ± 1) can be done in one cycle.
Example: r0 = r1 * 5 Example: r0 = r1 + (r1 * 4)
ADD r0, r1, r1, LSL #2
Example: r2 = r3 * 105 Example: r2 = r3 * 15 * 7 Example: r2 = r3 * (16 - 1) * (8 - 1) RSB r2, r3, r3, LSL #4 ; r2 = r3 * 15 RSB r2, r2, r2, LSL #3 ; r2 = r2 * 7
Notes: Main use for a shifted register is to provide inline multiplication (and division)
  Using one or more instructions with shifted registers.
This can often be quicker than using MUL instruction, though not as flexible.
  Need to know constant at compile / assemble time.
The problem of finding the optimum sequence becomes more difficult as constant becomes larger.
  No known algorithm to solve this problem quickly.
C compiler restricts amount of searching it does in order to minimise impact on compile time
  Has cut-off so that uses normal MUL once number of instructions used in squence passes a limit.
  Sequences could otherwise become very long.

## Slide 19: Multiplication Instructions
The Basic ARM provides two multiplication instructions.
Multiply
  MUL{<cond>}{S} Rd, Rm, Rs ; Rd = Rm * Rs
Multiply Accumulate - does addition for free
  MLA{<cond>}{S} Rd, Rm, Rs,Rn ; Rd = (Rm * Rs) + Rn
Restrictions on use:
  Rd and Rm cannot be the same register
    Can be avoid by swapping Rm and Rs around. This works because multiplication is commutative.
  Cannot use PC.
These will be picked up by the assembler if overlooked.
Operands can be considered signed or unsigned
  Up to user to interpret correctly.
Notes: One example of use of MLA is for string to number conversion:
eg/
  Convert string=“123” to value=123
  value = 0
  loop = 0
  len = length of string
  while loop <> len
  c = extract( string, len -loop,1)
  Rm = 10 ^ loop
  Rs = ASC(c) - ASC (‘0’)
  Rd = value
  MLA Rd, Rm, Rs, Rd
  loop = loop + 1
  endwhile

## Slide 20: Load / Store Instructions
The ARM is a Load / Store Architecture:
  Does not support memory to memory data processing operations.
  Must move data values into registers before using them.
This might sound inefficient, but in practice isn’t:
  Load data values from memory into registers.
  Process data in registers using a number of data processing instructions which are not slowed down by memory access.
  Store results from registers out to memory.
The ARM has three sets of instructions which interact with main memory. These are:
  Single register data transfer (LDR / STR).
  Block data transfer (LDM/STM).
  Single Data Swap (SWP).
Notes: All instructions other than these can only use values in registers

## Slide 21: Single register data transfer
The basic load and store instructions are:
  Load and Store Word or Byte
    LDR / STR / LDRB / STRB
ARM Architecture Version 4 also adds support for halfwords and signed data.
  Load and Store Halfword
    LDRH / STRH
  Load Signed Byte or Halfword - load value and sign extend it to 32 bits.
    LDRSB / LDRSH
All of these instructions can be conditionally executed by inserting the appropriate condition code after STR / LDR.
  e.g. LDREQB
Syntax:
  <LDR|STR>{<cond>}{<size>} Rd, <address>

## Slide 22: Load and Store Word or Byte: Base Register
The memory location to be accessed is held in a base register
  STR r0, [r1] ; Store contents of r0 to location pointed to ; by contents of r1.
  LDR r2, [r1] ; Load r2 with contents of memory location ; pointed to by contents of r1.
r1
0x200
Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
r2
0x5
Destination Register for LDR

## Slide 23: Load and Store Word or Byte: Pre-indexed Addressing
Example: STR r0, [r1,#12]
To store to location 0x1f4 instead use: STR r0, [r1,#-12]
To auto-increment base pointer to 0x20c use: STR r0, [r1, #12]!
If r2 contains 3, access 0x20c by multiplying this by 4:
  STR r0, [r1, r2, LSL #2]
r1
0x200
Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
Offset
12
0x20c

## Slide 24: Load and Store Word or Byte: Post-indexed Addressing
Example: STR r0, [r1], #12
To auto-increment the base register to location 0x1f4 instead use:
  STR r0, [r1], #-12
If r2 contains 3, auto-incremenet base register to 0x20c by multiplying this by 4:
  STR r0, [r1], r2, LSL #2
r1
0x200
Original Base Register
Memory
0x5
0x200
r0
0x5
Source Register for STR
Offset
12
0x20c
r1
0x20c
Updated Base Register