## Slide 1: Filesystems
CSCI 380
Operating Systems
Prof. William Killian

## Slide 2: Files and Directories

## Slide 3: Remember the Fundamentals…
User Abstraction |  | Hardware Resource
Processes/Threads | <= OS => | CPU
Address Space | <= OS => | Memory
Files | <= OS => | Disk

## Slide 4: File System Abstraction
Applications Daemons Servers Shell
------------- Application Programming Interface -------------
open() close() read() write() link() rename()
----------------- Device Independent Interface -----------------
Sectors Tracks seek() readBlock() writeBlock()
------------------------ Device Interface ------------------------
Hardware (SSD, HDD, SD-Card)

## Slide 5: User Requirements on Data
Fast – we don’t want to wait
Vast – we should be able to store all the things
Persistent – data stays around (imagine data loss after rebooting)
Safe – users should be able to keep files to themselves (protec) or share data with other users (sharing)
Easy – searching/examining/modifying data should be simple

## Slide 6: Hardware and OS Features
Fast Vast Persistent Safe Easy
Hardware Operating Systems

## Slide 7: User Requirements on Data
Fast – Enabling random access means faster data access
Vast – Disk sizes are constantly increasing (8TB HDD, 2TB SSD)
Persistent
  Disks provide magnetic storage. SSDs often use NVRAM.
  Redundancy within OS allows recovery from certain types of failures
Safe – Unix provides Read Write eXecute privileges on all files
Easy
  Names refer to files
  Files can be logically organized into directories
  Transparent (non-user-aware) mapping of files and directories onto hardware
  Search facilities in OSes (Spotlight, Cortana, etc)

## Slide 8: Files
File – Logical unit of data on a storage device
  ”A named collection of related information recorded on secondary storage”
  Ex: test.c, a.out, /bin/ls
Files can contain programs (source, binary) or data
Files can be structured or unstructured
  UNIX implements files as a sequence of bytes (unstructured)
File Attributes – additional information to store
  Name
  Type
  Location
  Size
  Permissions
  Creation Time, etc

## Slide 9: User Interface to the File System
Data Operations:
create() delete()
open() close()
read() write()
seek()
Naming Operations:
hardLink() softLink()
setAttribute() getAttribute()
rename()

## Slide 10: Creating a File
create(name)
  Allocate necessary disk space (checks quotas, permissions, etc)
  Create a file descriptor (include name, location, and attributes)
  Add the file descriptor to the directory containing the file
  Optionally add file type / other attributes

## Slide 11: Deleting a File
deleting(name)
  Find the directory containing the file
  Free the disk blocks used by the file
  Remove the file descriptor from the directory
  Behavior is dependent on hard links

## Slide 12: Open and Close
We have covered these previously…
fileID = open(name, mode)
close(fileID)
File permissions are checked
Remember: open counts get changed, file tables are updated

## Slide 13: Read
read(fileID, from, size, buf)
  OS reads “size” bytes from file position “from” into “buf”
  for (i = from; i < from + size; i++) {
  buf[i – from] = file[i];
read(fileID, size, buf)
  OS reads “size” bytes from current file position fp into buf, then advances fp
  for (i = 0; i < size; i++) {
  buf[i] = file[fp + i];
  fp += size;

## Slide 14: Write, Seek, Memory Map
write operations are similar to reads, but copies the other direction
seek just updates fp stored within the file descriptor
Memory mapping a file
  Maps part of the virtual address space to a file
  Read/write operations to that portion of memory implies OS read/write from corresponding location in the file
  File accesses are simplified (no read/write calls are necessary)

## Slide 15: File Access Methods
Programmer’s View:
Sequential: data processed in order
Most programs use this method
Ex: compiler reading a source file
Direct: address a block based on a key value
Databases often do this
Ex: hash table, dictionary
Operating System’s View:
Sequential: keep a pointer to the next byte in the file; update pointer on each read/write operation
Direct: address any block in the file directly provided its offset within the file

## Slide 16: Naming and Directories
We need a way to refer to files that are stored on disk
OS uses numbers for each file
  Users prefer textual names to refer to files
  Directory: OS data structure to map names to file descriptors
Naming Strategies:
  Single-Level Directory: one name space for the entire space, every name unique
    Use a special area of disk to hold directory (containing <name, index> pairs
  Two-Level Directory: each user has a separate directory, but all of each user’s files must still have unique names
  Multi-Level Directory: tree-structure name space (UNIX and all modern OSes)

## Slide 17: Multi-Level Directories
Store directories on disk, just like files
  Except file descriptor for directories have a special flag bit
User programs read directories just like any other file
  But only special system calls can write directories
Each directory contains <name, fileDesc> pairs in arbitrary order
  The file referred to by a name could be another directory
There is one special “root” directory
  /

## Slide 18: Referential Naming
Hard Links (UNIX: ln command)
  A hard link adds a second (or more) connection to a file
  Ex: creating a hard link from B to A
    Before: A  file #100
    After “ln A B”: A  file #100
    B  file #100
  OS maintains reference counts and deletes only when count == 0
Soft Links (UNIX: ln -s command)
  A soft link only makes a symbolic pointer from one file to another
    After “ln -s A B” A  file #100
    B  A
  Removing “A” leaves the name B in the directory, but its contents no longer exist

## Slide 19: Directory Operations
Search – locate an entry for a file in the current directory
Create – adds a directory listing
Delete – removes a directory listing
List – list all files (ls command in UNIX)
Rename -- renames a file (mv command in UNIX)
Traverse (recursive?)

## Slide 20: Protection
OS must allow users to control sharing of files
Grant or deny access to file operations depend on protection info.
Access Lists and Groups (Windows NT)
  Keep an access list for each file with username and type of access
  Lists can become large and tedious to maintain
Access Control Bits (UNIX)
  Three categories of user: owner, group, world
  Three types of access privileges: read, write, execute
  Maintain a bit for each combination: 111101000  rwxr-x---

## Slide 21: Summary of File System Functionality
Naming
Protection
Persistence
Fast

## Slide 22: How Physical Disks Work

## Slide 23: What’s Inside A Disk Drive?
Spindle
Arm
Actuator
Platters
Electronics
(including a
processor
and memory!)
SCSI
connector
Image courtesy of Seagate Technology

## Slide 24: Disk Geometry
Disks consist of platters, each with two surfaces.
Each surface consists of concentric rings called tracks.
Each track consists of sectors separated by gaps.
Spindle
Surface
Tracks
Track k
Sectors
Gaps

## Slide 25: Disk Geometry (Multiple-Platter View)
Aligned tracks form a cylinder.

## Slide 26: Disk Capacity
Capacity: maximum number of bits that can be stored.
  Vendors express capacity in units of gigabytes (GB) or terabytes (TB), where 1 GB = 109 Bytes and 1 TB = 1012 Bytes
Capacity is determined by these technology factors:
  Recording density (bits/in): number of bits that can be squeezed into a 1 inch segment of a track.
  Track density (tracks/in): number of tracks that can be squeezed into a 1 inch radial segment.
  Areal density (bits/in2): product of recording and track density.
Tracks

## Slide 27: Computing Disk Capacity
Capacity = (# bytes/sector) x (avg. # sectors/track) x
(# tracks/surface) x (# surfaces/platter) x
(# platters/disk)
Example:
  512 bytes/sector
  300 sectors/track (on average)
  20,000 tracks/surface
  2 surfaces/platter
  5 platters/disk
Capacity = 512 x 300 x 20,000 x 2 x 5
= 30,720,000,000
= 30.72 GB

## Slide 28: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
By moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle
spindle
spindle
spindle
spindle

## Slide 29: Disk Operation (Multi-Platter View)

## Slide 30: Disk Structure - top view of single platter
Tracks divided into sectors
Surface organized into tracks
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 31: Disk Access
Head in position above a track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 32: Disk Access
Rotation is counter-clockwise
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 33: Disk Access – Read
About to read blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 34: Disk Access – Read
After BLUE read
After reading blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 35: Disk Access – Read
After BLUE read
Red request scheduled next
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 36: Disk Access – Seek
After BLUE read
Seek for RED
Seek to red’s track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 37: Disk Access – Rotational Latency
After BLUE read
Seek for RED
Rotational latency
Wait for red sector to rotate around
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 38: Disk Access – Read
After BLUE read
Seek for RED
Rotational latency
After RED read
Complete read of red
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 39: Disk Access – Service Time Components
After BLUE read
Seek for RED
Rotational latency
After RED read
Data transfer
Seek
Rotational
latency
Data transfer
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 40: Disk Access Time
Average time to access some target sector approximated by:
Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tavg seek)
Time to position heads over cylinder containing target sector.
Typical Tavg seek is 3—9 ms
Rotational latency (Tavg rotation)
Time waiting for first bit of target sector to pass under r/w head.
Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
Typical Tavg rotation = 7,200 RPMs
Transfer time (Tavg transfer)
Time to read the bits in the target sector.
Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min.

## Slide 41: Disk Access Time Example
Given:
  Rotational rate = 7,200 RPM
  Average seek time = 9 ms.
  Avg # sectors/track = 400.
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4 ms.
  Tavg transfer = 60/7200 RPM x 1/400 secs/track x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms
Important points:
  Access time dominated by seek time and rotational latency.
  First bit in a sector is the most expensive, the rest are free.
  SRAM access time is about 4 ns/doubleword, DRAM about 60 ns
    Disk is about 40,000 times slower than SRAM,
    2,500 times slower then DRAM.

## Slide 42: Logical Disk Blocks
Modern disks present a simpler abstract view of the complex sector geometry:
  The set of available sectors is modeled as a sequence of b-sized logical blocks (0, 1, 2, ...)
Mapping between logical blocks and actual (physical) sectors
  Maintained by hardware/firmware device called disk controller.
  Converts requests for logical blocks into (surface,track,sector) triples.
Allows controller to set aside spare cylinders for each zone.
  Accounts for the difference in “formatted capacity” and “maximum capacity”.

## Slide 43: I/O Bus
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.

## Slide 44: Reading a Disk Sector (1)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
mouse
keyboard
Monitor
Disk
I/O bus
Bus interface
CPU initiates a disk read by writing a command, logical block number, and destination memory address to a port (address) associated with disk controller.

## Slide 45: Reading a Disk Sector (2)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
Disk controller reads the sector and performs a direct memory access (DMA) transfer into main memory.

## Slide 46: Reading a Disk Sector (3)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU).

## Slide 47: Solid State Disks (SSDs)
Pages: 512KB to 4KB, Blocks: 32 to 128 pages
Data read/written in units of pages.
Page can be written only after its block has been erased.
A block wears out after about 100,000 repeated writes.
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks

## Slide 48: SSD Performance Characteristics
Sequential access faster than random access
  Common theme in the memory hierarchy
Random writes are somewhat slower
  Erasing a block takes a long time (~1 ms).
  Modifying a block page requires all other pages to be copied to new block.
  In earlier SSDs, the read/write gap was much larger. Fixed by flash translation layer.
Sequential read tput 550 MB/s Sequential write tput 470 MB/s
Random read tput 365 MB/s Random write tput 303 MB/s
Avg seq read time 50 us Avg seq write time 60 us
Source: Intel SSD 730 product specification.

## Slide 49: SSD Tradeoffs vs Rotating Disks
Advantages
No moving parts  faster, less power, more rugged
Disadvantages
Have the potential to wear out
Mitigated by “wear leveling logic” in flash translation layer
E.g. Intel SSD 730 guarantees 128 petabyte (128 x 1015 bytes) of writes before they wear out
In 2015, about 30 times more expensive per byte
Applications
MP3 players, smart phones, laptops
Increasingly common in desktops and servers

## Slide 50: File System Implementation

## Slide 51: File Organization on Disk
fileID 0, Block 0  Platter 0, Cylinder 0, Sector 0
fileID 0, Block 1  Platter 4, Cylinder 3, Sector 8
Performance Issues:
  Support sequential and random access
  How to structure data to maintain file location information
  How do we physically lay out the files on the physical disk

## Slide 52: On-Disk Data Structures
File Descriptor
  The structure used to describe where the file is on the disk
  Also maintains a list of attributes of the file
  Must be stored on the disk just like all other files
Most Systems…
  Have a majority of small files
  Have the majority of disk space taken up by large files
  Have I/O operations target both small and large files
The per-file cost must be low, but large files must also have good perf.

## Slide 53: 1. Contiguous Allocation
OS maintains an ordered list of free blocks
OS allocates a contiguous chunk of free blocks when it creates a file
Need to store only the start location and size in the file descriptor
Advantages:
  Simple
  Access Time, Number of Seeks
Disadvantages:
  Changing file sizes
  Fragmentation, Disk management
Examples:
  IBM OS/360, write-once disks, early personal computers

## Slide 54: 2. Linked Files
Keep a list of all the free sectors/blocks
In the file descriptor, keep a pointer to the first sector/block
In each sector, keep a pointer to the next sector
data
link
data
link
data
link
data
link
data
link
P: 4
C: 20
S: 5
P: 2
C: 7
S: 1
P: 8
C: 12
S: 0
P: 1
C: 3
S: 9

## Slide 55: 2. Linked Files (continued)
Advantages
  Fragmentation
  File size changes
  Efficient support of _______ access
Disadvantages
  Does not support _______ access
  Number of seeks?
Examples:
  FAT, MS-DOS

## Slide 56: 3. Indexed Files
OS keeps an array of block pointers for each file
User (or OS) must declare maximum length of the file when created
OS allocates array to hold pointers to all blocks
  but only allocates blocks on demand
OS fills in the pointers as it allocates blocks
Advantages:
  Minimal wasted space for files
  Sequential/Random access easy
Disadvantages:
  Wasted space in FDs
  Maximum file size
  Lots of seeks due to non-contiguous data
FD Data
bp 0
bp 1
bp MAX

## Slide 57: 4. Multi-Level Indexed Files
Each FD contains k block pointers
First k-2 block pointers point to data
k-1th pointer points to a block of 2d pointers to 2d more data blocks
kth pointer points to a block of pointers to indirect blocks
Advantages:
  Incremental file growth
  Small files
Disadvantages:
  Indirect access is inefficient for Random Access
  Lots of seeks because non-contiguous data
Example: BSD UNIX 4.3

## Slide 58: Free Space Management
Need a way to keep track of which disk blocks are free
  *cough* malloc lab? *cough*
Need to be able to find free space quickly and release space quickly
Solution? Use a bitmap?
  The bitmap has one bit for each block on the disk.
  If the bit is 1, the block is free, else the bit is 0 and block is allocated
  Can quickly determin if any page in the next 32 is free (32-bit) but comparing to “word” 0
  Marking a block as freed is as simple as toggling a bit

## Slide 59: Free Space Management
Problem: bitmap might be too big to keep in memory for a large disk
  2TB disk with 512byte sectors requires a bitmap with 4G (4 billion) entries
  4Gb == 500MB
If most of the disk is in use, it will be expensive to find free blocks with a bitmap
An alternative implementation is to link together free blocks *cough*
  The head of the list is cached in kernel memory
  Each block contains a pointer to the next free block
  Costs for allocating? Freeing? Allocate consecutive blocks?

## Slide 60: Summary
Many of the concerns and implementations are similar to VM
  Contiguous allocation is simple, but suffers from:
    External fragmentation
    Need for compaction
    Need to move files as they grow
  Indexed allocation is analogous to page tables
    Table maps from logical file blocks to physical disk blocks
  Free space can be managed using a bitmap or a linked list

## Slide 61: Disk Head Scheduling (Antiquated)

## Slide 62: Disk Head Scheduling
Idea
  Permute the order of disk requests from the order they arrive to minimize number of length of seeks to perform
  First-Come, First-Serve (FCFS)
  Shortest Seek Time First (SSTF)
  SCAN algorithm (0..N, N..0, 0..N, …)
    If there is no request between current position and “extreme”, do not seek there
  C-SCAN circular scan algorithm (0..N, 0..N, 0..N, …)

## Slide 63: Disk Head Scheduling
FCFS
  No overhead, works well for light loads; also for SSDs
SSTF
  Always go to next closest request, maintain doubly linked sorted list
SCAN
  Service requests as we pass them (akin to an elevator)
  Requires sorted list of requests
C-SCAN
  Like SCAN, but once it hits the bottom or top, it jumps to the other end and moves in the same direction

## Slide 64: Bonus: RAID
Multiple disk drives can provide reliability through redundancy
  Also performance?
Disk striping uses a group of disks as one storage unit
Disk mirroring uses a group of disks as a smaller storage unit
There are 6 different levels of RAID